## Slide 1: Flash Settings in CCS 9.2.0

## Slide 2
In Workspace right click on the project file and select the Properties
Proj_lab01[Active – Release] -> Properties

## Slide 3
In Properties window select the option General and in that select Manage configuration to add the Flash setting.

## Slide 4
In Configuration Window Select New to Create New Configuration
In Create New Configuration, Add the Name and Description for reference when build the project
Once New configuration is Created the Manage Configuration Window will be Updated and Active.
1
2
3

## Slide 5
In Linker Command File add Linker Command File For F28069 Device.
TI\Motorware\motorware_1_01_00_18\sw\ide\ccs\cmd\f2806x

## Slide 6
In Include Option add all the files that are needed to build the project.

## Slide 7
Check whether all the Include files are added.

## Slide 8
Add the following flags set in the C2000 Linker and then Apply and Close.
-m"${ProjName}.map" --stack_size=0x3B0 --warn_sections -i"${CG_TOOL_ROOT}/lib" -i"${CG_TOOL_ROOT}/include" --priority --reread_libs --disable_auto_rts --diag_suppress=16002 --xml_link_info="${ProjName}_linkInfo.xml" --rom_model

## Slide 9
Check in the workspace for RAM/FLASH file added in the project